## Slide 1: Nixon Bohr
Created by: Jordan fluth and Vernon jones

## Slide 2: Inspiration
The idea for this project came after seeing a youtube video of a master’s thesis which used a Microsoft Kinect to control a LEGO NXT brick.
http://www.youtube.com/watch?v=FTBBlt9uk1A

## Slide 3: hardware required
A laptop with Bluetooth connection
A Microsoft Xbox Kinect
LEGO NXT Brick
Two TETRIX motor controllers
A TETRIX servo controller
12V battery

## Slide 4: Hardware Setup

## Slide 5: Software required
Microsoft Windows Operating System
ROBOTC IDE (30-day trial offered)
FAAST
Kinect development software

## Slide 6: Initial condition of robot
The initial condition was not great. It was a head and shoulders mounted on a motorized platform. All of our motor controllers were missing along with the LEGO NXT brick and the face skin was damaged beyond repair.

## Slide 7: Objective
Establish wireless serial communication between the laptop and the LEGO NXT brick over Bluetooth
Program gestures to be recognized by the Kinect and translated into physical movements on the robot for driving operations
Program gestures to be recognized by the Kinect and translated into physical movements on the robot for controlling the arm
Refine motion controls such that we can drive over to an object, pick it up and place it in a desired location

## Slide 8: Robot control state diagram
MOVE WHEELS
MOVE ARM
MOVE HAND
s
s
w
w
s

## Slide 9: Wheels
Wheels are controlled with two DC motors
Each motor can independently move forward/backward
Forward
Backward
Left
Right

## Slide 10: Move Wheel State diagram
STOP
FORWARD
BACKWARD
LEFT
RIGHT
f
b
r
b
f
f
b
r
l
l
l
r
All inputs of (s) will move to this state

## Slide 11: Movement demonstration

## Slide 12: Arm
The Arm consists of the shoulder and the elbow
Shoulder has 2 DOF, elbow has 1 DOF
Shoulder
Elbow

## Slide 13: ARM state diagram
IDLE
SHOULDER UP
ELBOW DOWN
SHOULDER DOWN
SHOULDER RIGHT
SHOULDER LEFT
ELBOW UP
i
J
z
x
k
m

## Slide 14: hand
The hand contains the wrist and the fingers
Wrist
Hand

## Slide 15: Hand state diagram
IDLE
HAND OPEN
WRIST RIGHT
HAND CLOSE
WRIST DOWN
WRIST UP
WRIST LEFT
A
e
g
h
c
d

## Slide 16: Arm demonstration

## Slide 17: results
Complete motor control of robot
  All motors and servos work
Complete control of arm with 6 degrees of freedom
  Continuous motion servos swapped out for 180° servos
New body gives Bohr more potential
  Looks more like a human, less like babyface
Added box to hide electrical components

## Slide 18: Results cont.
Robot can be controlled using keyboard input
  Bluetooth communication is hidden, only need to input keystrokes
Robot can be controlled using Microsoft Kinect
Ability to switch between arm mode, hand mode, and drive mode
Range of remote control: about 30ft

## Slide 19: Results demo: picking up bottle

## Slide 20: Visual Basic – auto-send character

## Slide 21: Visual Basic – Connect to BT

## Slide 22: Bluetooth mailbox

## Slide 23: Technical problems
Original plan involved Kinect and laptop mounted on robot
  Kinect requires 120VAC
  Extension cords??? No thanks…
Tried to make the robot autonomous, but ours sensors were stolen…
Too much weight for 12VDC motors
Continuous rotation servos don’t work well in RobotC
Bad left/right shoulder servo

## Slide 24: Future plans
Add parameter box in robot theater for people to be able to control Nixon Bohr
Add vision
Move arm to shoulder and add an identical arm on other side
Add facial emotion with IGA

## Slide 25: Hours spent
Jordan – Lots
Vernon – Lots

## Slide 26: Web pages

## Slide 27: Any questions?